1. Hardware specification of Picam v1 and Picam v2 :

https://www.raspberrypi.org/documentation/hardware/camera/

2. Raspberry Pi Camera v1.3 Features :

2.1 Image Process features:

2.1.1	Image Rotation :

If your preview was upside-down, You can rotate the image by 90, 180, or 270 degrees, or you can set it to 0 to reset.

2.1.2	Camera and Video Resolution :

The resolution of the capture is configurable.

The maximum resolution is 2592 x 1944 for still photos and 1920 x 1080 for video recording.
The minimum resolution allowed is 64 x 64.

Frame rate Maximum upto 90fps for Video recording.

2.1.3	Picture and Video format :

Picture formats	JPEG (accelerated), JPEG + RAW, GIF, BMP, PNG, YUV420, RGB888
Video formats	raw h.264 (accelerated)

2.1.4	Camera Brightness :

You can alter the brightness setting, which can be set from 0 to 100. The default is 50.

2.1.5	Annotation Text for Image :

If you want to give annotation text name on your Image.

Valid sizes are 6 to 160. The default is 32.

2.1.6	Annotation_Background , Annotation_Foreground and Image effect :

Annotation_Background and Annotation_Foreground and Image effects not useful for us.

2.1.7	Auto white balance mode :

To set the auto white balance to a preset mode.

The options are: off, auto, sunlight, cloudy, shade, tungsten, fluorescent, incandescent, flash, and horizon. The default is auto.

2.1.8	Exposure mode :

To set the exposure to a preset mode to apply a particular effect.

The options are: off, auto, night, nightpreview, backlight, spotlight, sports, snow, beach, verylong, fixedfps, antishake, and fireworks. The default is auto.

2.1.9	Capturing image Low loght :

Source : https://picamera.readthedocs.io/en/release-1.13/recipes1.html

the Pi’s camera can capture images in low light conditions.
The primary objective is to set a high gain, and a long exposure time to allow the camera to gather as much light as possible.

However, the shutter_speed attribute is constrained by the camera’s framerate so the first thing we need to do is set a very slow framerate.

The maximum the Pi’s V1 camera module is capable of 6 second exposure time ; the V2 camera module can manage 10 second exposures.

2.2 Video Process features :

2.2.1	Video Camera quality parameters :

The camera’s H.264 encoder is primarily constrained by two parameters:
- bitrate limits the encoder’s output to a certain number of bits per second. The default is 17000000 (17Mbps), and the maximum value is 25000000 (25Mbps). Higher values give the encoder more “freedom” to encode at higher qualities. You will likely find that the default doesn’t constrain the encoder at all except at higher recording resolutions.
- quality tells the encoder what level of image quality to maintain. Values can be between 1 (highest quality) and 40 (lowest quality), with typical values providing a reasonable trade-off between bandwidth and quality being between 20 and 25.
2.2.2 Recording over multiple files :
If you wish split your recording over multiple files, you can use the split_recording() method.
By this API we can split number of recording videos in certain time.

2.2.3 Video recording file converter :
You have to use a muxer like MP4Box after you've finished recording to create .mp4 files from raw .h264.
sudo apt-get install gpac

# Wrap the raw video with an MP4 container:

MP4Box -fps 30 -add infile.h264 outfile.mp4
omxplayer outfile.mp4
Convert file in mp4 by command :
Source : https://raspi.tv/2013/another-way-to-convert-raspberry-pi-camera-h264-output-to-mp4